## Slide 2
Definitions CPU,MPU,MCU,SOC:
CPU(central processing unit)/Processor : is a chip, assigned with the instructions of performing logical I/O operations and arithmetical functions of the computer. it contains millions of tiny transistors to run the system effectively.
Microprocessor chips (MPU) : are silicon devices that serve as the central processing unit (CPU) in computers. They contain thousands of electronic components and use a collection of machine instructions to perform mathematical operations and move data from one memory location to another. A Microprocessor is the latest form of processor or CPU. The microprocessor is a single-chip circuit integrated with all qualities of CPU with few new circuits. Its processing speed is greater than CPU. Today all latest processor CPUs are a microprocessor. It is developed for multipurpose. It is capable in accepting and storing data and process them in output as a result according to instructions.
Microcontroller Unit (MCU): is a small computer on a single VLSI integrated circuit (IC) chip, or is a small, self-contained computer that is housed on a single integrated circuit, or microchip. They differ from your desktop computer in that they are typically dedicated to a single function, and are most often embedded in other devices, a microcontroller contains one or more CPUs (processor cores) along with memory and programmable input/output peripherals. It is an intelligent semiconductor IC that consists of a processor unit, memory modules, communication interfaces and peripherals. The MCU is used across a broad range of applications, including washing machines, robots, drones, radio and game controllers.
System On Chip (SOC) : is a less well-defined term. It is a single chip package that does everything that previously required multiple chips. A SoC is typically an encapsulation of one or more of CPUs, memory, micro-controllers, DSPs, accelerators, and supporting hardware; however, it does not adhere to any standards regarding its containing circuitry. An SoC is intended for applications with requirements that are too complex for a single MCU to handle. There might be a number of micro-controllers in a SoC. It is more like a complete computer system on a single chip, capable of performing complex tasks with higher resource requirements. It is sometimes abbreviated as SoC or SOC.

## Slide 3
What are the three types of microprocessor?
There are three types of microprocessors namely, CISC, RISC, and EPIC.
What are the four primary operations of MPU?
It performs some basic operations like addition, subtraction, multiplication, division, and some logical operations using its Arithmetic and Logical Unit (ALU).
What is the difference between MCU MPU and CPU? : Microcontrollers (MCUs) tend to be less expensive, simpler to set-up, and simpler to operate than microprocessors (MPUs). An MCU can be viewed as a single-chip computer, whereas an MPU has surrounding chips that support various functions like memory, interfaces, and I/O.

## Slide 4
Microprocesseur vs microcontrôleur | Microprocessor | microcontroller
Applications | Personal computer, laptop(Gaming, web browsing, photos editing, creating documents, mathematical calculation, simulations) | Digital camera, washing machines, microwave oven
Use case | Can be used in light/intensive applications like creating a doc/gaming, thus the amount of memory required depends on tha application. Task not defined, depends on user | Specific task, based on the inputs(from user/sensors) which are given to the MC, it does somep processing
Internal structure | It only contains a CPU(central Processing unit), and all the interfaces(RAM, ROM, Serial, timers and I/O ports) are connected to it externally | The amount of resources is limited and these elements are integrated along with the CPU inside a single chip
Memory | Clock speed : 1GHZ to 4GHZ RAM : 512MB to 32GB ROM (Hard Disk): 128GB to 2TB Peripheral interfaces : USB, High Speed Ethernet, UART | Clock speed : 1MHZ to 300MHZ RAM : 2KB to 256KB Flash Memory : 32KB to 2MB Peripheral interfaces : I2C, SPI, UART
Unit | Capacity of 32bit and 64bit per reading | 8bit, 16bit and 32bit
Power consumption & cost | High | Low